## Slide 1
METHODOLOGY
MOTIVATION
Autonomous Driving is a promising technology to enhance road safety, to ease road congestion, decrease fuel consumption and free human drivers. In the architecture of autonomous driving, decision-making is a key component to realizing autonomy.
Autonomous cars need to take correct and safe decisions for driving in an urban environment without colliding with other agents. Decision-making algorithms for autonomous driving consists of heuristic-based and learning-based algorithms. We applied Deep Reinforcement Learning to solve the decision-making problem in autonomous driving to make safe lane changes in a simulated highway gym environment​.
INTRODUCTION
For our project, we have considered lane changing in a 4-lane highway scenario. Below image shows the real world and simulation environment.
Here our goal is to achieve maximum reward (covering maximum distance in shortest time) without any collision with other cars.
ENVIRONMENT
RESULTS
CONCLUSION
From the results, it can be observed that PPO learned to change the lanes early (in 800 episodes) as compared to DQN (1200 episodes). Also, mean reward for PPO (180) is greater than compared to DQN (90) after training. DDDQN, an improvement over DQN, eventually performed better than DQN as expected and earned 130 mean reward in 1300 episodes. DDPG, trained on continuous action-space took time for agent to follow the lane and earned 230 mean reward after 1200 episodes of learning.
Deep Reinforcement Learning for Decision Making in Autonomous Driving
Amey Deshpande, Bhushan Rane, Denny Boby, Yash Patil (Robotics)
Advisor : Professor Yanhua Li
This project uses highway-env environment which is part of Open AI Gym. It is an environment for autonomous driving and decision-making. There are various kinds of observation types which gives different data to train on, and different type of actions as mentioned:
Type of Observation:
Kinematics
Grayscale Image
Occupancy Grid
Time to Collision
Action Types:
Continuous Actions
Discrete Meta Actions
Manual Control Action
Deep Q-Network (DQN)
DDPG
Dueling Double DQN (DDDQN))
PPO
DDDQN
DDPG
PPO
Deep Q-Network (DQN)